## Slide 1: CIS454/554 Data Comm. Networks
Lecture 14
Wenbing Zhao

## Slide 2: Outline
Link layer devices
802.11 wireless LAN

## Slide 3: Link Layer Devices
Hubs
Switches

## Slide 4: Hubs
… physical-layer (“dumb”) repeaters:
  Bits coming in one link go out all other links at same rate
  All nodes connected to hub can collide with one another
  No frame buffering
  No CSMA/CD at hub: host NICs detect collisions
twisted pair
hub

## Slide 5: Switch
Link-layer device: smarter than hubs, take active role
  Store, forward Ethernet frames
  Examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent
  Hosts are unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured

## Slide 6: Switch: Allows Multiple Simultaneous Transmissions
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  Each link is its own collision domain
Switching: a-to-a’ and b-to-b’ simultaneously, without collisions
  Not possible with dumb hub
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 7: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
Looks like a routing table!
Q: how are entries created, maintained in switch table?
  Something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 8: Switch: Self-Learning
Switch learns which hosts can be reached through which interfaces
  When frame received, switch “learns” location of sender: incoming LAN segment
  Records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 9: Switch: Frame Filtering/Forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 10: Self-Learning, Forwarding: Example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
Frame destination unknown: flood
Destination A location known: selective send
A’ A
A’
4
60

## Slide 11: Interconnecting Switches
Switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 12: Institutional Network

## Slide 13: Switches vs. Routers
Both store-and-forward devices
  Routers: network layer devices (examine network layer headers)
  Switches are link layer devices
Routers maintain routing tables, implement routing algorithms
Switches maintain switch tables, implement filtering, learning algorithms

## Slide 14: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 15: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 16: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication
  will typically run DHCP to get IP address in AP’s subnet

## Slide 17: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
Active Scanning:
Probe Request frame broadcast from H1
Probes response frame sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent: selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
Passive Scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent: selected AP to H1

## Slide 18: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  Solution:
    Link layer acknowledgement
    Collision avoidance: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 19: IEEE 802.11 MAC Protocol: CSMA/CA: Link layer acknowledgement
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK
Notes: Difs: distributed inter-frame space
Sifs: short inter-frame spacing

## Slide 20: Avoiding Collisions: when ack is not received in time
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 21: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 22: Homework#4.9
Objective 9: Understand the switch self-learning protocol
Important concepts/knowledge (please elaborate each)
  Difference between Hubs and Switches
  How CSMA/CD is used in switches?
  How a switch is made transparent to hosts?
  Switch self-learning protocol
  When switches are interconnected together, how do they work together?
Problem: Suppose C sends frame to I, I responds to C, as shown in the figure below. Show switch tables and frame forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
1
2