## Slide 1: CIS454/554 Data Comm. Networks
Lecture 2
Wenbing Zhao
(Part of the slides are based on Drs. Kurose & Ross’s slides for their Computer Networking book)

## Slide 2: Outline
Internet structure
Network edge
  Hosts and applications
Network core
  Packet switching
Delay, loss and throughput in packet-switched networks

## Slide 3: A Closer Look at Internet Structure:
Network edge:
  Applications and hosts
Access networks, physical media:
  wired, wireless communication links
Network core:
  interconnected routers
  network of networks

## Slide 4: The Network Edge:
End systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
Client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
Peer-peer model
  minimal (or no) use of dedicated servers, e.g. Skype, BitTorrent

## Slide 5: Access Networks
Q: How to connect end systems to edge router?
residential access nets
  DSL, Cable Modem
institutional access networks (school, company)
mobile access networks
  Wifi
  3G, 4G, LTE

## Slide 6: The Network Core
Mesh of interconnected routers
The fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 7: Network Core: Circuit Switching
End-to-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 8: Network Core: Circuit Switching
Network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
Dividing link bandwidth into “pieces”
frequency division
time division

## Slide 9: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 10: Numerical Example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
Notes: Each circuit has a transmission rate of 1.536Mbps/24=64kbps, so it takes 640,000 bits/64kbps = 10 seconds to transmit the file. Adding .5sec circuit establishment time, it comes to 10.5 second per file. Here we ignored the propagation delay

## Slide 11: Network Core: Packet Switching
Each end-end data stream divided into packets
User A, B packets share network resources
Each packet uses full link bandwidth
Resources used as needed
Resource contention:
Aggregate resource demand can exceed amount available
Congestion: packets queue, wait for link use
Store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 12: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand  statistical multiplexing
TDM: each host gets same slot in revolving TDM frame
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
Statistical Multiplexing
queue of packets
waiting for output
link

## Slide 13: Packet-Switching: Store-and-Forward
Takes L/R seconds to transmit (push out) packet of L bits on to link at R bps
Store and forward: entire packet must arrive at router before it can be transmitted on next link
End to end delay = 3L/R (assuming zero propagation/processing/queueing delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
End-to-end delay = 15 sec
R
R
R
L
more on delay shortly …
Notes: The 3L/R emphasize on the delay caused by the store and forward strategy: the packet has to be transmitted 3 times:
- sender (end system) to 1st router
- 1st router to 2nd router
- 2nd router to receiver

## Slide 14: Packet Switching versus Circuit Switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link
Notes: Don’t’ worry how the number 0.0004 is derived

## Slide 15: Packet Switching versus Circuit Switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
Is packet switching a “slam dunk winner?”

## Slide 16: Internet Structure: Network of Networks
Roughly hierarchical
At center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  Treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 17: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 18: Internet Structure: Network of Networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 19: Internet Structure: Network of Networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 20: Internet Structure: Network of Networks
A packet passes through many networks!
EEC-484/584: Computer Networks
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 21: How Do Loss and Delay Occur?
Packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 22: Four Sources of Packet Delay
1. Processing delay:
check bit errors
determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. Queueing delay
time waiting at output link for transmission
depends on congestion level of router

## Slide 23: Delay in Packet-Switched Networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 24: Caravan Analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
Time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
Time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 25: Caravan Analogy
Cars now “propagate” at 1000 km/hr
Toll booth now takes 1 min to service a car
Q: Will cars arrive at 2nd booth before all cars serviced at 1st booth?
Yes! After 7 min, 1st car at 2nd booth and 3 cars still at 1st booth.
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
toll
booth
toll
booth
ten-car
caravan
100 km
100 km
Notes: Applet list: http://wps.aw.com/aw_kurose_network_5/111/28536/7305312.cw/index.html

## Slide 26: Nodal Delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 27: Queueing Delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 28: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 29: Packet Loss
Queue (aka buffer) preceding link in buffer has finite capacity
Packet arriving to full queue dropped (aka lost)
Lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
Applets: http://wps.aw.com/aw_kurose_network_3/21/5493/1406348.cw/index.html

## Slide 30: Throughput
Throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  Instantaneous: rate at given point in time
  Average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 31: Throughput (more)
Rs < Rc What is average end-to-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-to-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 32: Throughput: Internet Scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
Per-connection end-end throughput: min(Rc,Rs,R/10)
In practice: Rc or Rs is often bottleneck

## Slide 33: Homework#1.1
Objective 1: Able to understand the average throughput that can be achieved in the Internet
Key points:
  The Internet consists of multiple routers and many segments with different bandwidth
  The end-to-end average throughput is limited by the bottleneck link
  If a router with total bandwidth of R is connected to n networks, then it is shared by these n networks, and each network can only enjoy R/n bandwidth on average
Problem: Assume that R is connected to 20 servers and 20 end-users (i.e., the client). The bandwidth between each server and the router is Rs=10Mbps, and that between each end-user and the router is Rc=1Mbps, the router bandwidth R=1Gpbs. What is the average end-to-end throughput between the server and the client?