## Slide 1: CIS454/554 Data Comm. Networks
Lecture 6
Wenbing Zhao
(Part of the slides are based on Drs. Kurose & Ross’s slides for their Computer Networking book)

## Slide 2: Outline
Quiz#1 result
Introduction to transport layer
Multiplexing/demultiplexing
Reliable data transfer

## Slide 3: CIS454 Quiz#1 Result
Max: , Min: , Mean:
Q1: , Q2: , Q3: , Q4:
Wenbing Zhao
5/10/23

## Slide 4: Transport Layer
Our goals:
Understand principles behind transport layer services:
  multiplexing/ demultiplexing
  reliable data transfer
  flow control
  congestion control
Learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 5: Internet Transport-Layer Protocols
Reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
Unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
Services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 6: Multiplexing/Demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:
Notes: Ip enables comm between host and host

## Slide 7: How Demultiplexing Works
Host receives IP datagrams
  Each datagram has source IP address, destination IP address
  Each datagram carries 1 transport-layer segment
  Each segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 8: Connectionless Demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 9: Connectionless Demux
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 10: Connection-Oriented Demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 11: Connection-Oriented Demux
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
DP: 80
SP: 5775
D-IP:C
S-IP: B

## Slide 12: Connection-oriented demux: Multi-Threaded Web Server
Client
IP:B
P1
client
IP: A
P1
P2
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P4
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 13: Principles of Reliable Data Transfer
Important in app., Transport, link layers
Top-10 list of important networking topics!
Characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 14: Reliable Data Transfer: Getting Started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 15: Reliable Data Transfer: Getting Started
We’ll:
Incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
Consider only unidirectional data transfer
  but control info will flow on both directions!
Use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 16: rdt1.0: reliable transfer over a reliable channel
Underlying channel perfectly reliable
  No bit errors
  No loss of packets
Separate fsms for sender, receiver:
  Sender sends data into underlying channel
  Receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 17: rdt2.0: channel with bit errors
Underlying channel may flip bits in packet
  Checksum to detect bit errors
The question: how to recover from errors:
  Acknowledgements (acks): receiver explicitly tells sender that pkt received OK
  Negative acknowledgements (naks): receiver explicitly tells sender that pkt had errors
  Sender retransmits pkt on receipt of NAK
New mechanisms in rdt2.0 (beyond rdt1.0):
  Error detection
  Receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 18: rdt2.0: FSM specification
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 19: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 20: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 21: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
Handling duplicates:
sender retransmits current pkt if ACK/NAK garbled
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 22: rdt2.1: sender handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L
Notes: Stopped here for 1st session 10/1/2012

## Slide 23: rdt2.1: receiver handles garbled packets
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
Notes: Stopped here 10/2/2014 why does the receiver have to send ack in response to a duplicate data pkt

## Slide 24: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 25: rdt2.2: a NAK-free protocol
Same functionality as rdt2.1, using acks only
Instead of NAK, receiver sends ACK for last pkt received OK
  Receiver must explicitly include seq # of pkt being acked
Duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 26: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK0, chksum)
udt_send(sndpkt)

## Slide 27: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or acks)
  Checksum, seq. #, Acks, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
Retransmits if no ACK received in this time
If pkt (or ACK) just delayed (not lost):
  Retransmission will be duplicate, but use of seq. #’S already handles this
  Receiver must specify seq # of pkt being acked
Requires countdown timer

## Slide 28: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 29: rdt3.0 in action

## Slide 30: rdt3.0 in action

## Slide 31: Performance of rdt3.0
rdt3.0 works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 32: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R