## Slide 1: CIS454/554 Data Comm. Networks
Lecture 8
Wenbing Zhao
(Part of the slides are based on Drs. Kurose & Ross’s slides for their Computer Networking book)

## Slide 2: Outline
Reminder
  6/21: quiz#2
UDP
TCP
  Segment header structure
  Connection management
  Reliable data transfer
  Flow control
  Congestion control

## Slide 3: TCP: Overview
Full duplex data:
  Bi-directional data flow in same connection
  MSS: maximum segment size
Connection-oriented:
  Handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
Flow controlled:
  Sender will not overwhelm receiver
Point-to-point:
  One sender, one receiver
Reliable, in-order byte steam:
  No “message boundaries”
Pipelined:
  TCP congestion and flow control set window size
Send & receive buffers

## Slide 4: TCP: Overview
TCP connection is byte stream, not message stream, no message boundaries
TCP may send immediately or buffer before sending
Receiver stores the received bytes in a buffer
Notes: Stopped 10/3/2012 session 1

## Slide 5: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
A TCP segment must fit into an IP datagram!
Notes: Ask: why is there no length field?
Why receive window is there? Recall that TCP offers a duplex channel

## Slide 6: The TCP Segment Header
Source port and destination port: identify local end points of the connection
  Source and destination end points together identify the connection
Sequence number: identify the byte in the stream of data that the first byte of data in this segment represents
Acknowledgement number: the next sequence number that the sender of the ack expects to receive
  Ack # = Last received seq num + 1
  Ack is cumulative: an ack of 5 means 0-4 bytes have been received
TCP header length – number of 32-bit words in header
Notes: Ack#: instead of saying “I have received all bytes until ack#-1.”, we say: “the next expected byte number is ack#.”

## Slide 7: The TCP Segment Header
URG – indicates urgent pointer field is set
Urgent pointer – points to the seq num of the last byte in a sequence of urgent data
ACK – acknowledgement number is valid
SYN – used to establish a connection
  Connection request: ACK = 0, SYN = 1
  Connection confirm: ACK=1, SYN = 1
FIN – release a connection, sender has no more data
RST – reset a connection that is confused
PSH – sender asked to send data immediately
Notes: Taken from http://www.vijaymukhi.com/vmis/tcp.htm
The Urgent Pointer is used when some information has to reach the server ASAP. When the TCP/IP stack at the other end sees a packet using the Urgent Pointer, it is duty bound to stop all it's doing and immediately send this packet to the relevant server. Since the packet is plucked out of the processing queue and acted upon immediately, it is known as an Out Of Band (OOB) packet and the data is called Out Of Band (OOB) data. The Urgent Pointer is usually used in Telnet, where an immediate response (e.g. the echoing of characters) is desirable.

## Slide 8: The TCP Segment Header
Receiver window size –number of bytes that may be sent beyond the byte acked
Checksum – add the header, the data, and the conceptual pseudoheader as 16-bit words, take 1’s complement of sum
  For more info: http://www.netfor2.com/tcpsum.htm http://www.netfor2.com/checksum.html
Options – provides a way to add extra facilities not covered by the regular header
  E.g., communicate buffer sizes during set up

## Slide 9: TCP Sequence Numbers and ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet/ssh scenario
Notes: For tcp, seq # usually does not start from 0. If it were, we could interpret seq # as how many number of bytes of payload have been sent previously
Seq=43: seq field contain the next expected number even if the segment does not contain any payload

## Slide 10: TCP Connection Management
TCP sender, receiver establish “connection” before exchanging data segments
Initialize TCP variables:
  Sequence numbers
  Buffers, flow control info (e.g. RcvWindow)
Client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
Server: contacted by client
Socket connectionSocket = welcomeSocket.accept();

## Slide 11: TCP Connection Management
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial sequence number
  no data
Step 2: server host receives SYN, replies with SYN/ACK segment
  server allocates buffers
  specifies server initial sequence number
Step 3: client receives SYN/ACK, replies with ACK segment, which may contain data

## Slide 12: TCP Connection Management
Three way handshake:
SYN segment is considered as 1 byte
SYN/ACK segment is also considered as 1 byte
client
SYN (seq=x)
server
SYN/ACK (seq=y, ACK=x+1)
ACK (seq=x+1, ACK=y+1)
connect
accept

## Slide 13: TCP Connection Management
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 14: TCP Connection Management
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 15: TCP Reliable Data Transfer
TCP creates rdt service on top of IP’s unreliable service
Pipelined segments
Cumulative acks
TCP uses single retransmission timer
Retransmissions are triggered by:
  timeout events
  duplicate acks
Initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 16: TCP Sender Events:
Data rcvd from app:
Create segment with sequence number
seq # is byte-stream number of first data byte in segment
Start retransmission timer if not already running (think of timer as for oldest unacked segment)
Timeout:
retransmit segment that caused timeout
restart timer
Ack rcvd:
If acknowledges previously unacked segments
  update what is known to be acked
  restart timer if there are outstanding segment
Notes: Remember that ack is accumulative. If an ack number corresponding a seq number in the middle of the sending window, it is acking all bytes upto that ack number - 1

## Slide 17: TCP: Retransmission Scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
SendBase
= 100

## Slide 18: TCP: Retransmission Scenarios
Host A
Seq=100, 20 bytes data
ACK=100
time
premature timeout
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=92 timeout
ACK=120
Seq=92 timeout
SendBase
= 120
SendBase
= 120
Sendbase
= 100

## Slide 19: TCP Retransmission Scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
Cumulative ACK scenario
Host B
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120

## Slide 20: TCP ACK Generation
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap
Notes: To do: add illustrations for the above 4 scenarios

## Slide 21: TCP Flow Control
Receive side of TCP connection has a receive buffer:
Speed-matching service: matching the send rate to the receiving app’s drain rate
App process may be slow at reading from buffer
Flow control:
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast

## Slide 22: TCP Flow Control
(Suppose TCP receiver discards out-of-order segments)
Spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 23: Principles of Congestion Control
Congestion:
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)

## Slide 24: Approaches towards Congestion Control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control

## Slide 25: TCP Congestion Control: Additive Increase, Multiplicative Decrease
Approach: increase transmission rate (window size), probing for usable bandwidth, until loss occurs
  Additive increase: increase cwnd every RTT until loss detected
  Multiplicative decrease: cut cwnd after loss
Saw tooth
behavior: probing
for bandwidth
Notes: Basic idea

## Slide 26: TCP Congestion Control
Sender limits transmission:
LastByteSent-LastByteAcked
 cwnd
Roughly,
cwnd is dynamic, function of perceived network congestion
How does sender perceive congestion?
loss event = timeout or 3 duplicate acks
TCP sender reduces rate (cwnd) after loss event
rate =
cwnd
RTT
Bytes/sec
Notes: AIMD: Additive Increase, Multiplicative Decrease

## Slide 27: TCP Slow Start
When connection begins, cwnd = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  Initial rate = 2.5 kBps
Available bandwidth may be >> MSS/RTT
  Desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event
Notes: Restart next monday

## Slide 28: TCP Slow Start
When connection begins, increase rate exponentially until first loss event:
  Double cwnd every RTT
  Done by incrementing cwnd for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 29: Congestion Avoidance
Q: When should the exponential increase switch to linear?
A: When cwnd gets to 1/2 of its value before timeout
Implementation:
Variable Threshold
At loss event, Threshold is set to 1/2 of cwnd just before loss event
How to increase cwnd linearly: cwnd (new) = cwnd + mss*mss/cwnd

## Slide 30: Congestion Control
After 3 duplicated ACKs:
  cwnd is cut in half
  window then grows linearly
  Of course, retransmit segment (i.e., fast recovery/retransmit)
But after timeout event:
  cwnd instead set to 1 MSS
  window then grows exponentially
  to a threshold, then grows linearly
3 dup ACKs indicates network capable of delivering some segments
timeout indicates a “more alarming” congestion scenario
Philosophy:

## Slide 31: Summary: TCP Congestion Control
When cwnd is below Threshold, sender in slow-start phase, window grows exponentially
When cwnd is above Threshold, sender is in congestion-avoidance phase, window grows linearly
When a triple duplicate ACK occurs, Threshold set to cwnd/2 and cwnd set to Threshold
When timeout occurs, Threshold set to cwnd/2 and cwnd is set to 1 MSS

## Slide 32: TCP Sender Congestion Control
State | Event | TCP Sender Action | Commentary
Slow Start (SS) | ACK receipt for previously unacked data | cwnd = cwnd + MSS, If (cwnd > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of CongWin every RTT
Congestion Avoidance (CA) | ACK receipt for previously unacked data | cwnd = cwnd+ MSS * (MSS/cwnd) | Additive increase, resulting in increase of CongWin by 1 MSS every RTT

## Slide 33: TCP Sender Congestion Control
State | Event | TCP Sender Action | Commentary
SS or CA | Loss event detected by triple duplicate ACK | Threshold = cwnd/2, cwnd = Threshold, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
SS or CA | Timeout | Threshold = cwnd/2, cwnd= 1 MSS, Set state to “Slow Start” | Enter slow start
SS or CA | Duplicate ACK | Increment duplicate ACK count for segment being acked | CongWin and Threshold not changed

## Slide 34: TCP Congestion Control
Segment lost
Repeated acks
Slow start

## Slide 35: Homework 2.1
Objective 1: Able to understand the RDT3.0 reliable data transfer protocol
Key points:
  The protocol consists of two finite state machines (FSM), one for the sender, the other for the receiver
  The basic mechanisms that make reliable data transfer include checksum, receiver feedback, sender retransmission, duplicate detection (both for data packet at the receiver and for the ACK at the sender), countdown timer
  The protocol specification is described in terms of the FSM, which consists of the states at the sender and the receiver, and for each FSM, all possible events, and the corresponding actions, as well as the state transitions.
Problem. Consider the rdt3.0 protocol we have studied. The partial finite state machine for the receiver is shown (it is in fact identical to that of the rdt2.2 protocol):
Let’s say a student in the class studied the protocol and decided to change the protocol such that on receiving a duplicate or corrupt packet, no action is taken. What do you think about this modification of the rdt3.0 protocol? Is the new protocol going to be functioning correctly (i.e., can it ensure reliable data transfer under the same assumption of the original RDT3.0 protocol)? Please elaborate, that is, if you think the modified protocol still works, explain why omitting sending the ack when receiving a duplicate or corrupt packet does not matter, and on the other hand, if you think the protocol would stop working, describe a specific scenario that would violate the reliable data transfer guarantee.

## Slide 36: Homework 2.2
Objective 2: Able to understand the three-way handshake TCP connection mechanism
Key points:
  TCP connection establishment mechanism relies on the use of two flags SYN and ACK, and an initial sequence number, one from each direction
  SYN flag is turned on only for the very first message (i.e., connection request), while ACK is off
  The second message (connection confirmation) has SYN off and ACK flag on. All remaining messages has ACK on (and SYN off)
Problem. A process at host A wants to establish a TCP connection with another process at host B. Assuming that host A chooses to use 1628 as the initial sequence number, and host B chooses to use 3217 as the initial sequence number for this connection, show the segments involved with the connection establishment process. You must include the following information for each such segment: (1) sequence number, (2) acknowledgement number (if applicable), (3) the SYN flag bit status, and (4) the ACK flag bit status.

## Slide 37: Homework 2.3
Objective 3: Able to understand the TCP reliable data transfer mechanism
Key points:
  TCP operates on top of IP’s unreliable service
  TCP connection can be imaged to be streaming a sequence of bytes of payload, where each byte has a consecutive sequence number
  TCP uses pipelined segments, that is, sent multiple segments before stops for acknowledgment
  TCP uses cumulative acks, that is, the ack for # would mean that all bytes that have sequence number #-1 have been received
  TCP uses single retransmission timer
Problem: Host A and B are communicating over a TCP connection, and host B has already received from A all bytes up through byte 126. Suppose Host A then sends two segments to Host B back-to-back. The first and second segments contain 70 and 50 bytes of data, respectively. In the first segment, the sequence number is 127, the source port number is 302, and the destination port number is 80. Host B sends an ack whenever it receives a segment from Host A.
  In the second segment sent from A to B, what are the sequence number, source port number, and destination port number?
  If the first segment arrives before the second segment, in the ack of the first arriving segment, what is the ack number, the source port number, and the destination port number?
  If the second segment arrives before the first segment, in the ack of the first arriving segment, what is the ack number?
  Suppose the two segments sent by A arrive in order at B. The 1st ack is lost and the 2nd ack arrives after the 1st timeout interval. Draw a timing diagram showing these segments and all other segments and acks sent. (Assume there is no additional packet loss.) For each segment in your figure, provide the sequence number and the number of bytes of data; for each ack that you add, provide the ack number

## Slide 38: Homework 2.4
Objective 4: Able to understand TCP congestion control
Key points:
Initially, explore the network capacity aggressively from 1 segment (exponentially, double the window for every roundtrip time)
It uses a threshold parameter sshred to cap the exponential growth on transmission window (i.e., throughput)
The mechanism considers two different events as an indication for congestion: timeout (more serious) and triple duplicate ACK (less serious). On either event, cut ssthred to half of the previous value
  On timeout: start from 1 segment
  On 3 ACKs: start from new ssthred
Problem: Consider the figure here and answer the following questions.
  Identify the intervals of time when TCP slow start is operating
  Identify the intervals of time when TCP congestion avoidance is operating
  After the 16th transmission round, is segment loss detected by a triple duplicate ACK or by a timeout?
  After the 22nd transmission round, is segment loss detected by a triple duplicate ACK or by a timeout?
  What is the initial value of ssthresh at the 1st transmission round?
  What is the value of ssthresh at the 18th transmission round?
  What is the value of ssthresh at the 24th transmission round?
  During what transmission round is the 70th segment sent?
  Assuming a packet loss is detected after the 26th round by the receipt of a triple duplicate ACK, what will be the values of the congestion window size and of ssthresh?