## Slide 1: CIS454/554 Data Comm. Networks
Lecture 7
Wenbing Zhao
(Part of the slides are based on Drs. Kurose & Ross’s slides for their Computer Networking book)

## Slide 2: Outline
Reliable data transfer (continued)
Pipelining protocols
UDP

## Slide 3: CIS454 Quiz#1 Result
Max: 100, Min: 30, Mean: 64.6
Q1: 33.4/50, Q2: 5.4/10, Q3: 15.75/20, Q4: 10/20
Wenbing Zhao
6/12/2023

## Slide 4: CIS554 MWF Quiz#1 Result
Max: 100, Min: 12, Mean: 55.9
Q1: 30/50, Q2: 4.5/10, Q3: 11/20, Q4: 10/20
Wenbing Zhao
6/12/2023

## Slide 5: CIS554 T Th Quiz#1 Result
Max: 84, Min: 40, Mean: 65.1
Q1: 34.5/50, Q2: 5/10, Q3: 14.6/20, Q4: 11/20
Wenbing Zhao
6/12/2023

## Slide 6: Pipelined Protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: go-back-N, selective repeat

## Slide 7: Pipelining: Increased Utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 8: Pipelining Protocols
Go-back-N: big picture:
Sender can have up to N unacked packets in pipeline
Rcvr only sends cumulative acks
  Doesn’t accept packet if there’s a gap
Sender has timer for oldest unacked packet
  If timer expires, retransmit all unacked packets
Selective Repeat: big pic
Sender can have up to N unacked packets in pipeline
Rcvr acks individual packets
Sender maintains timer for each unacked packet
  When timer expires, retransmit only unack packet

## Slide 9: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for oldest in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window
Notes: The black bars as not usable sequence numbers are due to the windows size limit, NOT due to non-sequential receive concern!

## Slide 10: GBN: Sender Extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1)
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum) // start timer if first unacked pkt
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum) // no more unacked pkts
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 11: GBN: Receiver Extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 12: GBN in action

## Slide 13: Selective Repeat
Receiver individually acknowledges all correctly received pkts
  Buffers pkts, as needed, for eventual in-order delivery to upper layer
Sender only resends pkts for which ACK not received
  Sender timer for each unacked pkt
Sender window
  N consecutive seq #’s
  Again limits seq #s of sent, unacked pkts

## Slide 14: Selective Repeat: Sender, Receiver Windows

## Slide 15: Selective Repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N-1]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
Sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
Receiver

## Slide 16: Selective Repeat In Action
Notes: Stopped here 10/7/2014

## Slide 17: Selective Repeat: Dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?

## Slide 18: Non-Sequential Receive Problem
The problem is caused by the overlap of sequence number between the new receiving window and the old receiving window
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Overlap
Overlap
Notes:   Note: number buffers at receiver needs = w

## Slide 19: Non-Sequential Receive Problem
Solution:
  make sure no overlap when receiver advances its window
  Make window size w =1/2 range of seq numbers
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
No Overlap

## Slide 20: UDP: User Datagram Protocol
“No frills,” “bare bones” Internet transport protocol
“Best effort” service, UDP segments may be:
  Lost
  Delivered out of order to app
Connectionless:
  No handshaking between UDP sender, receiver
  Each UDP segment handled independently of others
Notes: Stop here 2/27/12

## Slide 21: Why is There a UDP?
No connection establishment (which can add delay)
Simple: no connection state at sender and receiver
Small segment header
No congestion control: UDP can blast away as fast as desired

## Slide 22: UDP
Often used for streaming multimedia apps
  Loss tolerant
  Rate sensitive
Other UDP uses
  DNS
  SNMP
Reliable transfer over UDP: add reliability at application layer
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header
Notes: Simple Network Management Protocol (SNMP)

## Slide 23: UDP Checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Notes: Technical details for checksum computation not required

## Slide 24: Homework 2.1
EEC-484/584: Computer Networks
Wenbing Zhao
Objective 1: Able to understand the RDT3.0 reliable data transfer protocol
Key points:
  The protocol consists of two finite state machines (FSM), one for the sender, the other for the receiver
  The basic mechanisms that make reliable data transfer include checksum, receiver feedback, sender retransmission, duplicate detection (both for data packet at the receiver and for the ACK at the sender), countdown timer
  The protocol specification is described in terms of the FSM, which consists of the states at the sender and the receiver, and for each FSM, all possible events, and the corresponding actions, as well as the state transitions.
Problem. Consider the rdt3.0 protocol we have studied. The partial finite state machine for the receiver is shown (it is in fact identical to that of the rdt2.2 protocol):
Let’s say a student in the class studied the protocol and decided to change the protocol such that on receiving a duplicate or corrupt packet, no action is taken. What do you think about this modification of the rdt3.0 protocol? Is the new protocol going to be functioning correctly (i.e., can it ensure reliable data transfer under the same assumption of the original RDT3.0 protocol)? Please elaborate, that is, if you think the modified protocol still works, explain why omitting sending the ack when receiving a duplicate or corrupt packet does not matter, and on the other hand, if you think the protocol would stop working, describe a specific scenario that would violate the reliable data transfer guarantee.