## Slide 1
Lecture 9
Wenbing Zhao
(Part of the slides are based on Drs. Kurose & Ross’s slides for their Computer Networking book)
CIS454/554 Data Comm. Networks

## Slide 2: Outline
Quiz#2 result
Introduction to network layer
  Routing and forwarding, etc.
Router architecture
Routing algorithm
  Link state routing
  Distance vector routing

## Slide 3: CIS454 Quiz#2 Result
Max: 100, Min: 45, Mean: 68.9
Q1: 37.5/50, Q2: 6/10, Q3: 16.2/20, Q4: 9.2/15

## Slide 4: CIS554 MWF Quiz#2 Result
Max: 100, Min: 40, Mean: 61.1
Q1: 28.9/50, Q2: 5.2/15, Q3: 18.1/20, Q4: 8.9/15

## Slide 5: CIS554 TTh Quiz#2 Result
Max: 85, Min: 25, Mean: 51
Q1: 28.7/50, Q2: 3.3/15, Q3: 10.7/20, Q4: 8.3/15

## Slide 6: Network Layer
Main concern: end-to-end transmission
  Perhaps over many hops at intermediate nodes
Services provided to transport layer
  Transport segment from sending to receiving host
  On sending side encapsulates segments into datagrams
  On receiving side, delivers segments to transport layer
Network layer protocols in every host, router
Router examines header fields in all IP datagrams passing through it
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 7: Two Key Network-Layer Functions
Routing: determine route taken by packets from source to destination
Forwarding: move packets from router’s input to appropriate router output
Analogy:
Routing: process of planning trip from source to destination
Forwarding: process of getting through single intersection

## Slide 8: Interplay between Routing & Forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Forwarding table is
also referred to as routing table

## Slide 9: Network Service Model
Q: What service model for “channel” transporting datagrams from sender to receiver?
Example services for individual datagrams:
Guaranteed delivery
Guaranteed delivery with less than 40 msec delay
Best effort
Example services for a flow of datagrams:
In-order datagram delivery
Guaranteed minimum bandwidth to flow
Restrictions on changes in inter-packet spacing
No guarantee whatsoever

## Slide 10: Network Layer Connection and Connection-less Service
Datagram network provides network-layer connectionless service
Virtual Circuit network provides network-layer connection-oriented service (omitted)

## Slide 11: Datagram Networks
No call setup at network layer
Routers: no state about end-to-end connections
  no network-level concept of “connection”
Packets forwarded using destination host address
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
1. Send data
2. Receive data
application
transport
network
data link
physical

## Slide 12: Routing within a Datagram Subnet
Router has forwarding table telling which outgoing line to use for each possible destination router
Each datagram has full destination address
When packet arrives, router looks up outgoing line to use and transmits packet

## Slide 13: Datagram or VC Network: Why?
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing requirement
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
ATM (VC)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 14: What’s in a Router?
Run routing algorithms/protocol (RIP, OSPF, BGP)
Forwarding datagrams from incoming to outgoing link

## Slide 15: Input Port Functions
Decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory
queuing: newly arrived datagrams might be queued before processing
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet

## Slide 16: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission

## Slide 17: Routing Algorithms
Least-cost in what sense?
  Number of hops, geographical distance, least queueing and transmission delay
Desirable properties
  Correctness, simplicity
  Robustness to faults
  Stability – converge to equilibrium
Routing algorithm: algorithm that finds least-cost path

## Slide 18: Routing Algorithm Classification
Static or dynamic?
Non-adaptive (static) - Route computed in advance, off-line, downloaded to routers
Adaptive (dynamic) - Route based on measurements or estimates of current traffic and topology

## Slide 19: Routing Algorithm Classification
Global or decentralized information?
Global:
  all routers have complete topology & link cost info
  “link state” algorithms
Decentralized:
  router knows physically-connected neighbors, link costs to neighbors
  iterative process of computation, exchange of info with neighbors
  “distance vector” algorithms

## Slide 20: Link State Routing
Basic idea
Assumes net topology & link costs known to all nodes
  Accomplished via “link state broadcast”
  All nodes have same info
Computes least cost paths from one node (‘source”) to all other nodes, using Dijkstra’s Algorithm
  Gives forwarding table for that node

## Slide 21: Dijkstra’s Algorithm
Each node labeled with distance from source node along best known path
Initially, no paths known so all nodes labeled with infinity
As algorithm proceeds, labels may change reflecting shortest path
Label may be tentative or permanent, initially, all tentative
When label represents shortest path from source to node, label becomes permanent

## Slide 22: Compute Shortest Path from A to D
Start with node A as the initial working node
Examine each of the nodes adjacent to A, i.e., B and G, relabeling them with the distance to A
Examine all the tentatively labeled nodes in the whole graph and make the one with the smallest label permanent, i.e., B. B is the new working node
Notes: Steps computing the shortest path from A to D, using Dijkstra’s algorithm. The arrows indicate the working node.
We start out by marking node A as permanent, indicated by a filled-in circle. Then we examine, in turn, each of the nodes adjacent to A (the working node), relabeling each one with the distance to A. Whenever a node is relabeled, we also label it with the node from which the probe was made so that we can reconstruct the final path later. Having examined each of the nodes adjacent to A, we examine all the tentatively labeled nodes in the whole graph and make the one with the smallest label permanent. This one becomes the new working node.
Last two steps: C(9,B) permanent; D(10,H) permanent;

## Slide 23: Compute Shortest Path from A to D
Notes: Stopped here step3

## Slide 24
Step | Permanently labeled | B | G | E | C | F | H | D
1 | A | 2,A | 6,A | ∞ | ∞ | ∞ | ∞ | ∞
2 | AB |  | 6,A | 4,B | 9,B | ∞ | ∞ | ∞
3 | ABE |  | 5,E |  | 9,B | 6,E | ∞ | ∞
4 | ABEG |  |  |  | 9,B | 6,E | 9,G | ∞
5 | ABEGF |  |  |  | 9,B |  | 8,F | ∞
6 | ABEGFH |  |  |  | 9,B |  |  | 10,H
7 | ABEGFHC |  |  |  |  |  |  | 10,H
8 | ABEGFHCD |  |  |  |  |  |  | 

## Slide 25: Computation Results
B
C
D
E
F
G
H
(A,B)
(A,B)
(A,B)
(A,B)
(A,B)
(A,B)
(A,B)
Destination
link
A
B
C
D
E
F
G
H
Routing Table in A

## Slide 26: Home#3.1
Objective 1: Able to understand how to use Dijkstra’s Algorithm to find the first the shortest path for a network
Key points
  The algorithm works in rounds
  In each round, a new path is found, as the result, the distance previously labeled may have to be updated, that is, a previous longer path might now become shorter via this new path
  The algorithm terms once all nodes in the network have been considered
Problem: Given the subnet shown below, using the Dijkstra’s Algorithm, determine the shortest path tree from node u and its routing table
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5