## Slide 1: CIS454/554 Data Comm. Networks
Lecture 12
Wenbing Zhao
Cleveland State University

## Slide 2: Outline
7/3/2023
Data Link layer
  Error Detection and Correction
DLL
Data Link
Medium Access Control (MAC)

## Slide 3: CIS454 Quiz#3 Result
Max: 100, Min: 17, Mean: 79.3
Q1: 38.75/50, Q2: 16.7/20, Q3: 14.75/20, Q4: 9.2/10
Wenbing Zhao
7/3/2023

## Slide 4: CIS554 MWF Quiz#3 Result
Max: 95, Min: 15, Mean: 54.2
Q1: 28/50, Q2: 10/20, Q3: 8.4/20, Q4: 7.8/10
Wenbing Zhao
7/3/2023

## Slide 5: CIS554 TTh Quiz#3 Result
Max: 100, Min: 33, Mean: 76.8
Q1: 41.7/50, Q2: 11.9/20, Q3: 15.7/20, Q4: 7.5/10
Wenbing Zhao
7/3/2023

## Slide 6: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: done!
instantiation and implementation of various link layer technologies

## Slide 7: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 8: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 9: Link Layer Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already
  seldom used on low bit-error link (fiber, some twisted pair)

## Slide 10: Link Layer Services
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 11: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
  Ethernet card, PCMCI card, 802.11 card
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 12: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 13: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 14: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0
Example: Given 1011010
  With even parity  10110100
  With odd parity  10110101

## Slide 15: Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi)
Notes: Start here on wed

## Slide 16: CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R
R = remainder[ ]
D.2r
G

## Slide 17: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 18: Multiple Access protocols
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  Collision if node receives two or more signals at the same time
Multiple access protocol
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  No out-of-band channel for coordination

## Slide 19: MAC Protocols: Classification
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions

## Slide 20: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame

## Slide 21: Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 22: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  ALOHA
  slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 23: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit:
If channel sensed idle: transmit entire frame
If channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 24: CSMA collisions
collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes
note:
role of distance & propagation delay in determining collision probability

## Slide 25: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength

## Slide 26: CSMA/CD Collision Detection

## Slide 27: Homework#4.1
Objective 1: Understand Error Detection Mechanisms in Datalink Layer
Important concepts/knowledge (please elaborate each)
  Error detection principle
  Parity checking mechanism, parity bit
  Cyclic redundancy check (CRC) mechanism, CRC generator, modulo 2 division
Problem 1: If even parity is used, and a station A wants to transmit 1101101 to B, which parity bit should A append to its frame?
Problem 2: A bit stream 10011101 is to be transmitted using the standard CRC method described in the text. The generator polynomial is 1001. Show the actual bit string transmitted. Suppose the third bit from the left is inverted during transmission. Show that this error is detected at the receiver's end.

## Slide 28: Homework#4.2
Objective 2: Understand Multiple Access Links and Protocols
Important concepts/knowledge (please elaborate each)
  Types of data links
  The multiple access (MAC) problem, collision, collision recovery
  Classification of MAC protocols: channel partitioning (TDMA, FDMA), random access
Problem: For multi access control, there are two approaches, those based on channel partitioning, and those based on random access. In packet switching, there are two rather similar approaches as well, namely, circuit switching and package switching. Discuss the similarities and differences in these two problem domains and the corresponding approaches.

## Slide 29: Homework#4.3
Objective 3: Understand Random Access Protocols
Important concepts/knowledge (please elaborate each)
  CSMA, Collision detection, CSMA/CD
Problem 1: Consider two stations, A and B, in a datalink network. A is 1km away from B. The signal propagation speed is 200,000 km/second. The datalink has a bandwidth of 100Mbps. The packet size is fixed at 1024 Bytes. Answer the following questions:
  What is the transmission time for each packet?
  What is the propagation delay between A and B?
Problem 2: To detect a collision, a station must first receive the collision signal from the place of collision, and it takes a small amount of time for the station to determine that indeed a collision has occurred based on the collision signal received. Assume that the latter is 1 microsecond. Answer the following questions (assuming the condition from problem 1 still applies):
  If A and B happen to transmit a packet at the same time, how long does it take for A (or B) to receive the collision signal since the start of the transmission of the packet?
  If CSMA/CD is used, how much time can the station save compared against CSMA?